## Slide 1
Embedded Software Process
Author. NghiaNV16
Aug 31 2023

## Slide 2
CONTENT
2
Embedded software development
1
Embedded software overview
1
3
Embedded software process
© Copyright FPT Software – Level of Confidentiality

## Slide 3
01. Embedded software overview

## Slide 4: Embedded Software Overview
Embedded software is computer software, written to control machines or devices that are not typically thought of as computers.
It is typically specialized for the particular hardware that it runs on and has time and memory constraints.
This term is sometimes used interchangeably with firmware

## Slide 5: What is needed to start?
Development board
Debug Adapter
IDE and Software packet
Documents
S32K144 Reference Manual
Cortex M4 Device Generic User Guide
S32K144 Datasheet
S32K144EVB User Guide
S32K144EVB Schematic

## Slide 6: What is needed to start?

## Slide 7: Embedded Software Features
Quite limited resources
Acts directly with and on the hardware

## Slide 8
02. Embedded software development

## Slide 9: Embedded Software Build Process

## Slide 10: Embedded Software Build Process

## Slide 11: Reset Sequence
Vector Table | …. | ….
 | 0x0000.0004 | &Reset_Handler() – ex. 0x500
 | 0x0000.0000 | Reset Value of Stack Pointer
Processor will start here
Text Code | …. | ….
 | 0x1000 | void main() { main code }
 | 0x500 | void Reset_handler(void) { Startup Code main() }
 | …. | ….
PC = 0x500

## Slide 12: Embedded Software Components
Startup File
  Vector Table
  Startup Code/Reset_Handler()
Linker Script File
Application Code
  Main Code
  Library Code
Startup Code
Setup Stack Pointer
Init .bss section
Copy data Flash to RAM
Call main() function
Vector Table
main() and application code
Initialized data
Initialized data
Un-Initialized data
Heap
Stack
RAM
FLASH

## Slide 13: Startup Code

## Slide 14
03. Embedded software process

## Slide 15: Problem?
Design a Micro-Controller Project for DataLogger
  Read Sensor by ADC Peripheral (Ex. Temperature)
  Calculate Data – Convert to Physical Value – Temperature
  Display Data to LCD
  Save 10 lastest values

## Slide 16: Solution 1 - Polling
Advantage
  Simple to implement
Dis-Advantage
  Low performance
  Waste energy
  Can't do other things

## Slide 17: Solution 2 - Interrupt
Advantage
  Can do other things
  Save energy
  Prioritize important events
Dis-Advantage
  More complex
  Difficulty in debugging

## Slide 18: Solution 3 – DMA – Direct Memory Access
Advantage
  Can do other things
  Save energy
  Save CPU time
Dis-Advantage
  More complex

## Slide 19
CONTACT US
FPT Cau Giay Building, Duy Tan Street, Dich Vong Hau Ward, Cau Giay District, Hanoi City, Vietnam
Contact Person: Nghia Nguyen Van
Email: NghiaNV16@fpt.com